## Slide 1: WIFI learning

## Slide 2: Big picture
When STA connects to AP with RSNA, the phases are
  Discovery (finds the AP)
  Authentication + Association (link level connection)
  4-way handshake (secure key establishment)
STA
AP
Probe Request
Probe Response
STA
AP
Authentication Request
Authentication Response
Association Request
Association Response
STA
AP
Anounce + RSNE + replay counter
SNonce + RSNE + MIC
GTK (encrypted using PTK) + RSNE + MIC
Acknowledgment
Association request: STA请求加入AP的网络，包含RSNE，即STA支持的安全参数
Association Response: AP接受或拒绝，分配唯一标识符AID，AP的RSNE
这里采用的时Open system auth, 如果采用PSK auth，则分为4步

## Slide 3: Pre-shared key auth
PMK=PBKDF2(passphrase,SSID,4096,256 bits)，
4096,256 bits是PBKDF2的参数，代表迭代次数和输出长度
Passphrase就是password
Auth Request
Send challenge r
Challenge response
Ack
PSK auth本质上是在验证对方手中有PSK

## Slide 4: 802.1X EAP Authentication (替代PSK auth，适用于WPA2/WPA3-Enterprise)
Active Directory Server
(a Database that keeps track of all authorized users)
STA
AP
Radius server
Active Directory server
EAP start
EAP request identity
EAP response
Ports
Blocked
Open uncontrolled ports to allow EAP traffic
Radius access request
Checks database to make sure it’s authorized identity
Radius server似乎只是一个中继站
Sends challenge
Challenge Response
Correct
EAP success
A master session key (MSK) is generated on STA and Radius server after this process.
This master session key will be used to derive PMK
PMK
这样每个STA都与AP共享独有的PMK

## Slide 5
EAPol key frames

## Slide 6: SAE Auth (点对点密码认证，适用于WPA3-personal)

## Slide 7: 4 way handshake
Prequisite:
  AP and STA already share a PMK(private master key)
Process:
  AP generates random number Anounce, and sends Anounce to STA
  STA generates Snounce, and computes PTK = PRF(PMK, “Pairwise key generation”||Anounce||Snounce||AA||SA)
In practice AA and SA are sorted, Anounce and Snounce are sorted